## Slide 1
Old school with a twist: Intelligent electronic devices
Cristian Nicola
Lead developer @ Talis
http://www.talis.com
cn@talis.com
shared innovation

## Slide 2
Does anybody likes to tinker with things?
... Or to mend things?

## Slide 3
Does anybody likes “electronics”?

## Slide 4: Why bother ... ?
WorldWide Microcontroller Shipments (in millions of dollars)
'90 '91 '92 '93 '94 '95 '96 '97 '98 '99 '00
4-bit 1,393 1,597 1,596 1,698 1,761 1,826 1,849 1,881 1,856 1,816 1,757
8-bit 2,077 2,615 2,862 3,703 4,689 5,634 6,553 7,529 8,423 9,219 9,715
16-bit 192 303 340 484 810 1,170 1,628 2,191 2,969 3,678 4,405
Average Semiconductor Content per Passenger Automobile (in Dollars)
'90 '91 '92 '93 '94 '95 '96 '97 '98 '99 '00
$ 595 634 712 905 1,068 1,237 1,339 1,410 1,574 1,852 2,126
Company | 2008 Revenue ($ in millions)
Microchip Technology (MCHP) | 1035.7
Atmel Corporation (ATML) | 1567
STMicroelectronics (STM) | 9842

## Slide 5: What is a microcontroller ...
Highly integrated chip which includes, on one chip, all or most of the parts needed for a controller:
CPU (central processing unit)
RAM (Random Access Memory)
EPROM/PROM/ROM (Erasable Programmable Read Only Memory)
I/O (input/output)
serial and parallel timers interrupt controller
- Started as big complex analog monstrosities
- Later built exclusively from logic components - usually large, heavy boxes
- microprocessors were used and the entire controller could fit on a small circuit board (Zilog Z80, Intel 8088, Motorola 6809).
“A one chip computer”!
Typically has bit manipulation instructions, easy and direct access to I/O and quick and efficient interrupt processing
...cost is relatively low
Microcontrollers are a "one-chip solution" which drastically reduces parts count and design costs.

## Slide 6: Flavours
4, 8, 16, or 32 bit microcontrollers
specialized processors are available with features specific for communications
    keyboard handling
    signal processing
    video processing
    etc

## Slide 7: What to expect in a chip ...

## Slide 8: Architectural features ...
Von-Neuman Microcontrollers - a single "data" bus that is used to fetch instructions and data. Program and data stored in a common main memory
Harvard Architecture Microcontrollers - separate data bus and an instruction bus thus allows execution to occur in parallel; pre-fetch instructions allows for much faster execution than a Von-Neuman architecture with added silicon complexity
CISC - Complex Instruction Set Computer - has well over 80 instructions, many of them very powerful and very specialized for specific control tasks; many of the instructions are macro-like
RISC - Reduced Instruction Set Computers - smaller chip, smaller pin count, and very low power consumption - usally Harvard architecture (separate buses for instructions and data)
SISC - Specific Instruction Set Computer (SISC) - the idea was to limit the capabilities of the CPU itself, allowing a complete computer (memory, I/O, interrupts, etc) to fit on the available real estate

## Slide 9: Memory...
EEPROM - Electrically Erasable Programmable Read Only - relatively slow, and the number of erase/write cycles allowed in its lifetime is limited.
FLASH (EPROM) Flash provides a better solution than regular EEPROM when there is a requirement for large amounts of non-volatile program memory. It is both faster and permits more erase/write cycles than EEPROM.
Battery backed-up static RAM is useful when a large non-volatile program and DATA space is required. A major advantage of static RAM is that it is much faster than other types of non-volatile memory so it is well suited for high performance application.
Field programming/reprogramming Using nonvolatile memory as a place to store program memory allows the device to be reprogrammed in the field without removing the microcontroller from the system that it controls
OTP - One Time Programmable - a PROM (Programmable Read-Only-Memory) device
Software protection Either by encryption or fuse protection, the programmed software is protected against unauthorized snooping (reverse engineering, modifications, piracy, etc.)

## Slide 10: Power management ...
Low voltage parts - most microcontrollers only support 4.5 - 5.5 V operation – sometimes down to 3 volt (and lower)
Paul K. Johnson (of Hewlett-Packard) - rules of thumb regarding transistors:
The amount of power they dissipate is proportional to their size. If you make a transistor half as big, it dissipates half as much power.
Their propagation delay is proportional to their size. If you make a transistor half as big, it's twice as fast.
Their cost is proportional to the square of their size. If you make them half as big, they cost one quarter as much.
Brownout Protection - on-board protection circuit that resets the device when the operating voltage is lower than the brownout voltage
Idle/Halt/Wakeup - placed by software control - the state of the microcontroller remains –typically around 30% of normal power requirements
Multi-Input Wakeup - used to return (wakeup) the microcontroller from either HALT or IDLE modes

## Slide 11: I/O (1)...
UART (Universal Asynchronous Receiver Transmitter) serial port adapter for asynchronous serial communications.
USART (Universal Synchronous/Asynchronous Receiver Transmitter) serial port adapter for either asynchronous or synchronous serial communications.
SPI (Motorola) An SPI (serial peripheral interface) is a synchronous serial port.
SCI (serial communications interface) enhanced UART (asynchronous serial port).
I2C bus - Inter-Integrated Circuit bus (Philips) simple 2 wire serial interface
MICROWIRE/PLUS (National Semiconductor) serial synchronous bi-directional communications interface
CAN & J1850 CAN (Controller Area Network) is a mutiplexed wiring scheme that was developed jointly by Bosh and Intel for wiring in automobiles
I2S Integrated Interchip Sound, or IIS, is an electrical serial bus interface standard used for connecting digital audio

## Slide 12: I/O (2)...
Analog to Digital Conversion (A/D) Converts an external analog signal (typically relative to voltage) and converts it to a digital representation
Succesive Approximation A/D converters - the most common type of A/D and is used in the majority of microcontrollers
Single Slope A/D converters - you can build yourself - would include Analog Mux / comparator / timer (8-bit timer = 8 bit A/D - 16-bit timer = 16 bit A/D) with input capture and a constant current source
Delta-Sigma A/Ds converters - found on higher-end DSPs – using decimation and a filter is often called a "comb filter".
Flash A/D - basic architecture for the fastest category of A/Ds
D/A (Digital to Analog) Converters - takes a Digital number and converts it to a analog output
Pulse accumulator - an event counter
Input Capture can measure external frequencies or time intervals by copying the value from a free running timer into a register when an external event occurs.
Comparator One or more standard comparators can sometimes be placed on a microcontroller die.
Mixed (Analog-Digital) Signal analog quantity - pressure, temperature, voltage, current, air and water flow are always analog entities. They can be digitized for more efficient sorting, storage and transmittal, but the interface - the input and output - is almost always analog.

## Slide 13: Interrupts ...
Interrupts Polling
Interrupts - can be edge selectable (rising or falling) or level triggered.
Maskable Interrupts - one that you can disable or enable (masking it out means disabling the interrupt),
Global Interrupt Enable (GIE) allows you to turn off (or on) all of the maskable interrupts with one bit
Vectored interrupts - when an interrupt occurs, the hardware interrupt handler automatically branches to a specific address
Interrupt arbitration and priority

## Slide 14: Special features ...
Watchdog timer - provides a means of graceful recovery from a system problem (e.g. endless loop)
Digital Signal Processors (DSP) - execute repetitive math-intensive algorithms (e.g. MACC - Multiply and ACCumulate)
Clock Monitor - can shut the microcontroller down if the input clock is too slow
Resident program loader - Loads a program by Initializing program/data memory from either a serial or parallel port. Convenient for prototyping or trying out new features, eliminates the erase/burn/program cycle typical with EPROMs, and allows convenient updating of a system even from an offsite location.
Monitor A monitor is a program installed in the microcontroller which provides basic development and debug capabilities. Typically includes: loading object files into system RAM, executing programs, examining and modifying memory and registers, code disassembly, setting breakpoints, and single-stepping through code
Can either communicate with a dumb terminal or with a host computer such as a PC

## Slide 15: Microchip PIC ...
PIC - the first RISC microcontrollers.
Simple design - allows more features to be added at lower cost
Few instructions (eg. 33 instructions for the 16C5X line versus over 90 for the Intel 8048),
Separate buses for instructions and data (Harvard architecture) allows simultaneous access of program and data, and overlapping of some operations for increased processing performance
Very small chip, small pin count, and very low power consumption
Low cost, small size

## Slide 16: What are the PIC numbers ...
PIC or dsPIC followed a two-digit number, some letters, and then a two or three digit number
Next there can be a letter (A, B etc) indicating a revision, an/or a letter T indicating that the chips are on a tape (SMD only).
can be followed by a dash followed by a two-digit number and/or a letter that indicates the temperature range.
there can be a slash followed by a packaging indication.
first number can be 12, 16, 17, 18 or 30. 30 is for the 24-bit core dsPIC's. 18 is for PICs with a 16-bit core, 17 for PICs with different 16-bit core, 12 is for other PICs with 8 pins, and 16 is for all the rest. The 12 and 16 prefixes are used for both PICs with 12-bit and 14-bit cores.
The letter can be C or F, with some additions. C is for OTP (One Time Programmable) PICs, the F is for Flash (electrically reprogrammable) types.
CR (instead of just C) indicates a ROM (factory programmed) chip. CE indicates a C-type chip with a separate EEPROM chip in the same package.
An L can be added to idicate a low-voltage chip. Such chip can operate on lower voltages than their normal brothers, but often (always?) have a lower maximum clock frequency.
Summary: C = OTP (EPROM) CR = ROM CE = OTP + EEPROM F = FLASH LF = Low Voltage Flash LC = Low Voltage OTP LCR = Low Voltage ROM

## Slide 17: Tools - hardware

## Slide 18: Development boards...

## Slide 19: ICSP ...
ICSP = In Circuit Serial Programming (sometimes: ICP = In Circuit Programming)

## Slide 20: Tools - software

## Slide 21: The fun part...

## Slide 22: Special thanks to ...
http://uk.farnell.com/
http://uk.rs-online.com/
Iulian Ionescu – “Julianuary”
liviu.ionescu@gmail.com
For their huge stock of parts...
For many hours spent answering my silly questions...

## Slide 23
PIC18F2550
8BIT FLASH MCU, 18F2550, SDIL28
EEPROM Memory Size:256Byte
RAM Memory Size:2048Byte
No. of Timers:4
No. of PWM Channels:2
Operating Temperature Range:-40°C to +85°C
No. of Pins:28
Clock Frequency:48MHz
Flash Memory Size:32KB
Interface Type: EUSART, I2C, SPI, USB
Logic Function Number:18F2550
Supply Voltage:4.2V - 5.5V
Microprocessor/Controller Features: SPI, I²C, 2 x CCP, EUSART, 2 x Comparators, 1 x 8-bit timer, 3 x 16-bit timer
No. of ADC Inputs:10
No. of I/O Lines:24
No. of Internal Interrupts:19
Number of bits In Timer:16
Number of bits in ADC:10

## Slide 24
Bouncing

## Slide 25: Questions?

## Slide 26: Big thank you!